## Slide 1: Modern sewage treatment
Dr. M.V.Ajith Kumar
Prof & HoD
Dept of Community Medicine
SKHMC

## Slide 2: Modern sewage treatment
Modern sewage treatment plants are based on biological principles of sewage purification, where the purification is brought about by the action of anaerobic and aerobic bacteria.

## Slide 3: Sewage treatment
The treatment of sewage divided into two stages, primary treatment and secondary
treatment.
in secondary treatment, the
effluent is subjected to aerobic oxidation, which is the
second stage in purification

## Slide 4: primary treatment
In primary treatment, the solids are separatedfrom the sewage partly by screening and partly by sedimentation and subjected to anaerobic digestion
3 stages
  Screening
  Grit chamber
  Primary sedimentation

## Slide 5: Secondary treatment
It is subjected to further treatment, aerobic oxidation, by one of the following methods :
2 stages
First stage - one of the following method
(a} Trickling filter method
(b) Activated sludge process.
Second stage
Secondary sedimentation

## Slide 7: Other methods of sewage disposal
Sea outfall
River outfall
Land treatment
Oxidation ponds
Oxidation ditches

## Slide 8: Sludge digestion
The sludge is a thick, black mass containing 95 per cent of water, and it has a revolting odour.
methods of sludge disposal :
(a) Digestion
(b) Sea disposal
(c) Land :

## Slide 9: Digestion
sludge is incubated underfavourable conditions of temperature and pH in asludge digestion tank
anaerobic auto-digestion in which complex solids are broken down into water, carbon dioxide, methane and ammonia.
3-4 weeks or longer for complete sludge digestion.
Methane gas- by-product of sludge
Digestion- used for heating and lighting purposes

## Slide 10: OTHER METHODS OF SEWAGE DISPOSAL
(a) Sea outfall
(b) River outfall
(c) Land treatment
(d) Oxidation ponds
(e) Oxidation ditches.

## Slide 11: Disposal Of Effluent
Disposal by dilution
Disposal on land

## Slide 12: Other methods of sewage disposal
Sea outfall
River outfall
Land treatment
Oxidation ponds
Oxidation ditches

## Slide 13: REFERENCE
Park's Text Book of Preventive & Social Medicine