## Slide 1: REFUSE DISPOSAL
Dr .M.V.Ajithkumar
Prof& HoD
Community Medicine

## Slide 2: DISPOSAL OF WASTES
Types of Solid wastes
-Garbage – Food wastes
-Rubbish – paper, plastics, wood, metals, throw away
containers, glass.
- Demolition products- Bricks , Masonry, Pipes etc..
- Sewage treatment residue – sludge and solids from
the coarse screening of domestic sewage.

## Slide 3
Solid wastes are responsible for health hazards
a. It decomposes and favours fly breeding.
b. It attract rodent and vermin.
c. The pathogens which may be present in the solid waste may be conveyed back to man’s food through flies and dust. d. possibility of solid and water pollution.
e. Heaps of refuse present an unsightly appearance and nuisance from bad odours

## Slide 4: Sources of Refuse
Street refuse –Leaves, straw, paper
Market refuse –Putrid vegetables, animal matter
Stables refuse-Animal droppings, left over animal feeds.
Industrial refuse-Various inert materials such as calcium carbonate and other toxic substances.
Domestic refuse - Ash, rubbish, garbage

## Slide 5: Removal of Solid Wastes
1. Storage
2. Collection.
3. Methods of disposal

## Slide 6: Removal Of Solid Wastes
1.Storage –
First stage.
Galvanized dust bins are using commonly.
The size of bin depend upon number of users and frequency of collection.
A recent innovation is paper sacks.
The wastes are stored in these paper sacks and is removed with the contents for disposal.

## Slide 7: 2.Collection
Method of collection depends on fund required.
Best method is - house to house collection.
The refuse then transported in refuse collection vehicles to ultimate place of disposal.
A closed type refuse cart is using for carrying these wastes.

## Slide 8: 3.Methods of disposal
The choice of method depends on local factors such as
cost and availability of land
labour.

## Slide 9: Methods Of Refuse Disposal
1. Dumping –
2. Controlled tipping or sanitary land fill
a. the trench method,
b. the ramp method and
c.the area method

## Slide 10: Methods Of Refuse Disposal
1.Dumping –
Open areas are used for depositing the solid wastes.
Following are the drawbacks of dumping.; ( a) the refuse is exposed to flies and rodents,
(b) it is a source of nuisance from the smell and unsightly appearance
(c) the loose refuse is dispersed by the action of the wind
(d) drainage from dumps contributes to the pollution of surface and ground water.

## Slide 11: Methods Of Refuse Disposal
2.Controlled tipping or sanitary land fill –
It is the most satisfactory method of refuse disposal. Here a trunch or prepared area is used for disposal.It is of 3 types.
a. the trench method,
b. the ramp method and
c.the area method

## Slide 12
Trench method-
A long trench is dug out - 2 to 3 m (6-10 ft.) deep and 4 to 12 m, (12-36 ft.) wide, depending upon local conditions. The refuse is compacted and covered with excavated earth, where compacted refuse is placed in the fill to a depth of 2 m (6 ft.).
The ramp method-
This method is well suited where the terrain is moderately sloping. Some excavation is done to secure the covering material.

## Slide 13
c. The area method:
This method is used for filling land depressions, disused quarries and clay pits.
The refuse is deposited, packed and consolidated in uniform layers up to 2 to 2.5 m (6-8 ft.) deep. Each layer is sealed on its exposed surface with a mud cover at least 30 cm (12 inches) thick. Such sealing prevents infestation by flies and rodents and suppresses the nuisance of smell anddust.

## Slide 14
3. Incineration-
Hospital refuse is disposed of by incineration.
It is a high temperature dry oxidation process and it reduces organic and combustible waste to inorganic incombustible matter and results in very significant reduction of waste volume and weight.

## Slide 15: 4. Composting
is a method of combined disposal of refuse and nightsoil or sludge.
It is a process of nature whereby organic matter breaks down under bacterial action resulting in the formation of relatively stable humus-like material, called compost.
The principal by-products are CO2, H2O and heat.
The heat produced during composting, about 60 Оc or higher, over a period of several days, destroys eggs and larvae of flies, weed seeds and pathogenic agents.
The compost is a good soil builder containing small amounts of the major plant nutrients such as nitrates and phosphates .

## Slide 16: Methods of composting
(1) Bangalore method (Anaerobic method)
(2) Mechanical composting (Aerobic method)

## Slide 17
(1)Bangalore method of composting-
Trenches are dug 90 cm deep, 1.5 to 2.5 m broad and 4.5 to 10 m long,.
composting procedure is as follows :
First a layer of refuse about 15 cm thick is spread at the bottom of the trench. Over this, nightsoil is added corresponding to a thickness of 5
Then alternate layers of refuse and nightsoil are added in the proportion of 15 cm and 5 cm respectively, till the heap rises to 30 cm above the ground level.
The top layer should be of refuse, at least 25 cm thickness.
Within 7 days as a result of bacterial action considerable heat (is generated in the compost mass.
At the end of 4 to 6 months, decomposition is complete and the resulting in manure formatiom

## Slide 18
(2) Mechanical composting-
The refuse is first cleared of indigestable materials such as rags, bones, metal, glass and items which are likely to interfere with the grinding operation.
It is then pulverised in a pulverising equipment in order to reduce the size of articles to less than 2 inches.
The pulverised refuse is then mixed with sewage, sludge or nightsoil in a rotating machine and incubated.
The entire process of composting is complete in 4 to 6 weeks.

## Slide 19
4. Manure pits-
The problem of refuse disposal in rural areas can be solved by digging manure pits by individual house holders.
The garbage, cattle dung, straw, and leaves should be dumped into the manure pits and covered with earth after each day's dumping.
Two such pits will be needed, when one is closed, the other will be in use.
In 5 to 6 month's time, the refuse is converted into manure which can be returned to the field.

## Slide 20: 5. Burial-
This method is suitable for small camps.
A trench 1.5 m wide and 2 m deep is excavated, and at the end of each day the refuse is covered with 20 to 30 cm of earth.
When the level in the trench is 40 cm from ground level, the trench is filled with earth and compacted, and a new trench is dug out.
The contents may be taken out after 4 to 6 months and used on the fields. If the trench is 1 m in length for every 200 persons, it will be filled in about one week .